## Slide 1: Travel Behaviour Reconsidered in an Era of Decarbonisation
David Metz
UCL Centre for Transport Studies

## Slide 3: The need to reconsider travel behaviour
Understand the scope for reducing travel to help meet Net Zero objective
Question assumptions about travel behaviour that underlie orthodox transport economic appraisal and modelling

## Slide 4: Car dependence (1)
Car responsible for 61% of trips and 77% of distance travelled in 2019
76% of households own at least one car
Two thrusts to critique
  Places: eg new housing on greenfield sites with no alternative to the car
  People who prefer the car when active modes and public transport available
Critique has been widely endorsed by planners and academics, but has had little impact on car ownership and use
Problems of high level of car use well recognized, but attractions tend to be underestimated:
  Utility in getting from A to B, when congestion is not too severe and parking possible and affordable at both ends of trip
  Feel good factors
  Low marginal costs of operation

## Slide 5: Car dependence (2)
Car vehicle-miles-travelled
    80% from trips of more than 5 miles
    95% from trips of more than 2 miles
Predominance of the car reflects the low density built environment that we have inherited, within which nearly all trip origins and destinations occur – travel is a derived demand
New build housing adds only about 1% pa to stock
Some repurposing possible through changes to planning
Accommodating population growth and housing shortage:
  on greenfield sites, means more car use
  on urban brownfield, infill and ‘gentle densification’ – public transport more important
  in new towns – freestanding or urban extensions
Implications
  Attractions of the car and the inherited built environment limit scope for behavioural change that would reduce car use
  Best opportunities in cities where rail/trams are competitive with travel on congested roads
  Transport decarbonisation to be achieved very largely through electrification

## Slide 7: Mode share in Copenhagen and London
Chart: 
| Cycling | Car | Public transport | Walking
Copenhagen | 28 | 32 | 19 | 21
London | 2.5 | 35 | 36 | 25

## Slide 8: Impact of the pandemic

## Slide 9: Trends in Travel per capita
Chart: 
| 1972 | 1975 | 1978 | 1985 | 1990 | 1993 | 1996 | 1999 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019
trips/10 | 95.6 | 93.5 | 109.7 | 102.4 | 109.4 | 106 | 109.4 | 107.4 | 107.4 | 106 | 105.4 | 107 | 106.7 | 99.8 | 101.4 | 99.7 | 98.2 | 97.2 | 97.1 | 94.3 | 94.2 | 93.4 | 95.4 | 97.5 | 98.6 | 95.7
miles/10 | 447.6 | 474 | 479.1 | 531.7 | 650.6 | 654 | 698.3 | 715.9 | 719.3 | 721.1 | 706 | 718.2 | 710.9 | 713.3 | 688.8 | 671.6 | 669.8 | 676.4 | 660.7 | 659.2 | 649.6 | 665.7 | 649.9 | 658 | 653 | 650
time hr | 353 | 330 | 377 | 337 | 373 | 365 | 372 | 380 | 390 | 389 | 388 | 393 | 392 | 384 | 381 | 379 | 373 | 368 | 365 | 368 | 365 | 372 | 367 | 377 | 377 | 370

## Slide 10: Explaining travel trends
Invariant average per capita travel time since humans settled in communities
Travelling further in invariant time attributed to faster travel made possible by fossil fuel energy
The benefits of investment in faster travel taken as greater access (not the saving of travel time)
Growth ceased at turn of century because:
  New technology no longer allows faster travel
  Saturation of demand for travel

## Slide 11: Older transport technologies

## Slide 12: Newer transport technologies

## Slide 13: Access to supermarkets
80% of UK urban population have choice of 3 or more large supermarkets within 15 min drive, 60% have 4 or more
Generally, those with a car in the household, and/or decent public transport, have good levels of choice of regularly used destinations

## Slide 14: Access
Subject to diminishing returns
Increases with square of speed of travel
Therefore travel demand saturates – per capita travel ceases to increase
Travel time savings not a good proxy for access benefits
Economic appraisal needs to compare access in the with- and without-investment cases
Increased access implies more VMT and externalities, including carbon, than if benefits were taken as time saving

## Slide 15: Transport system maturity
Travel demand saturation implies a presumption that transport system is mature
  Accepted for urban roads
  Propose for interurban roads
  Maintain and make best use of existing infrastructure

## Slide 16: Interurban traffic
Congestion at peak flow prompts highway engineers to propose capacity increase
But morning and afternoon peaks indicate use by commuters, who have other choices

## Slide 17: Commuters have choices of route
New capacity attracts local traffic
Facilitated by digital navigation (satnav)
Can’t build our way out of congestion
Prediction of journey times - the best means of reducing uncertainty arising from congestion
Case study is an example of test of predictive validity of model – which failed

## Slide 18: Problems with transport modelling
Models are complex and opaque, understood only by experts
Lack of predictive validation – comparing outturn with forecast at sufficient granularity
Inability to model changes in access
So traffic model outputs are constrained to a counterfactual case which disregards changes in access
Conclusion: models cannot be relied on to estimate economic benefits or carbon emissions

## Slide 19: Analysis of mature networks
Economic analysis and modelling to focus on operations of road network, not investment in new capacity
Exploit wide use of digital navigation (satnav) to improve operational management and modelling of road network
Consider additional capacity only as part of proposals to access land brought into new uses.

## Slide 20: Conclusions
Future travel demand
  no need to plan for per capita growth,
  plan to accommodate population growth
Higher density of new homes allows more choice of travel modes
Treat road network as generally mature and make best use by means of digital technologies
Recognise limited attractions for car owners of active travel and public transport
Mitigate harms from car use, eg 20mph zones, LTNs, satnav
Transport decarbonisation effected largely by means of electric propulsion

## Slide 21
https://uclpress.co.uk/book/travel-behaviour-reconsidered-in-an-era-of-decarbonisation/
david.metz@ucl.ac.uk